## Slide 1
CASE-GEN-014 | TECHNICAL SYSTEMS EXPLAINER
Vapor-Compression
Heat Pumps
Move heat from a colder reservoir to a warmer space
by adding compressor work to a refrigerant loop.
Outdoor coil
absorbs heat
Indoor coil
releases heat
Compressor
work input
Expansion
pressure drop
Q_cold
Q_hot
W_in
Key idea for this deck
A heat pump does not create heat from nothing.
It uses a compressor to move heat along a refrigerant cycle.
Source: Vapor-compression heat pump notes | editable SVG components, arrows, and text
01 / 09
Notes: Use this opening slide to set the key mental model: a heat pump moves heat by adding work to a refrigerant cycle. Point out the three distinct energy arrows. Blue is heat absorbed from the cold reservoir, pink is compressor work input, and orange is useful heat delivered indoors. Emphasize that the deck never treats the system as creating heat from nothing.

## Slide 2
The Energy Balance to Remember
A heat pump uses work to move heat; it is not a heat-from-nothing machine.
Cold reservoir
outdoor air
heat is available, even when air is cold
Heat pump
cycle
compressor adds work to the loop
Warm space
indoor heating
useful heat delivered indoors
Q_cold
W_in
Q_hot
Q_hot = Q_cold + W_in
The machine delivers moved heat plus compressor work as indoor heat.
Legend: blue = absorbed heat, orange = delivered heat, pink = work input
02 / 09
Notes: Walk through the energy balance from left to right. Heat is absorbed from the outdoor reservoir as Q_cold, the compressor adds W_in, and the indoor space receives Q_hot. The relationship Q_hot = Q_cold + W_in is a qualitative accounting frame for heating mode. It explains why useful heat delivered indoors can be larger than the electrical work input alone.

## Slide 3
Five Components in One Refrigerant Loop
Each component changes either heat transfer, pressure, temperature, or flow direction.
HEATING MODE HARDWARE VIEW
Evaporator
absorbs heat
low pressure mixture to vapor
Condenser
releases heat
hot vapor to liquid
Compressor
adds work
pressure and temperature rise
Expansion valve
drops pressure
liquid cools before evaporator
Reversing
valve
switches modes
outdoor heat
indoor heat
electric work
Role checklist
Evaporator absorbs heat
Compressor raises pressure
Condenser releases heat
Expansion valve lowers pressure
Reversing valve swaps mode
No component is optional in the cycle logic.
Editable component blocks and arrows distinguish refrigerant flow, heat flow, and work input.
03 / 09
Notes: Introduce the five named components before discussing detailed thermodynamics. The evaporator absorbs heat and evaporates low-pressure refrigerant. The compressor raises pressure and temperature by adding work. The condenser releases heat and condenses vapor into liquid. The expansion valve lowers pressure before the refrigerant returns to the evaporator. The reversing valve changes the routing so the same hardware can support heating or cooling mode.

## Slide 4
Heating-Mode State Sequence
Follow the refrigerant state, not only the equipment names.
1
Outdoor evaporator
cold low-pressure mixture
becomes vapor
absorbs outdoor heat
2
Compressor
low-pressure vapor becomes
hot high-pressure vapor
work input
3
Indoor condenser
hot vapor condenses into
high-pressure liquid
releases heat indoors
4
Expansion valve
pressure drops; no useful work output
vapor
hot vapor
high-pressure liquid
cold low-pressure mixture
Heating mode: outdoor side absorbs heat; indoor side releases heat.
The compressor supplies the pressure lift.
Source-derived state sequence; expansion valve is pressure drop, not useful work output.
04 / 09
Notes: Read the loop as a four-step heating sequence. In the outdoor evaporator, a cold low-pressure mixture absorbs outdoor heat and becomes vapor. The compressor turns that low-pressure vapor into hot high-pressure vapor. The indoor condenser releases heat to the room as the vapor condenses into high-pressure liquid. The expansion valve then drops pressure and temperature before the refrigerant returns to the outdoor evaporator. Note that the expansion valve does not produce useful work.

## Slide 5
Heating vs Cooling Mode
The reversing valve changes which coil absorbs heat and which coil releases heat.
Heating mode
Goal: release heat indoors
Outdoor coil
evaporator
absorbs heat
Indoor coil
condenser
releases heat
heat in from outdoor air
heat out to room
Reversing valve routes flow
Cooling mode
Goal: absorb heat from the room
Outdoor coil
condenser
rejects heat
Indoor coil
evaporator
absorbs room heat
heat in from room
heat rejected outdoors
Same hardware, reversed roles
Mode switch = coil roles swap.
The loop still needs compressor, expansion, evaporation, and condensation.
The comparison is qualitative and source-grounded; arrows show directionality and heat interaction.
05 / 09
Notes: Use the split diagram to compare modes. In heating, the indoor coil acts as the condenser and releases heat indoors, while the outdoor coil acts as the evaporator. In cooling, those roles swap: the indoor coil absorbs heat from the room and the outdoor coil rejects it outdoors. The compressor and expansion processes still remain part of the same vapor-compression logic.

## Slide 6
COP: Why Greater Than 1 Is Possible
COP compares heat moved to compressor work input.
Heating performance
COP_heating = Q_hot / W_in
How much indoor heat is delivered per unit of compressor work.
Cooling performance
COP_cooling = Q_cold / W_in
How much room heat is removed per unit of compressor work.
Moved heat explains COP above 1
Q_cold
heat
absorbed
W_in
work
Q_hot
heat
delivered
COP is not capped like direct electric resistance efficiency.
Interpretation guardrail: high COP means heat is being moved efficiently, not created from nothing.
Editable formulas remain as text; no raster formula image is used.
06 / 09
Notes: Define both COP formulas as ratios between heat moved and work input. For heating, COP_heating is Q_hot divided by W_in. For cooling, COP_cooling is Q_cold divided by W_in. Stress that COP above one is not a violation of conservation of energy. It happens because the system is moving heat, not directly converting every unit of electricity into newly created heat.

## Slide 7
Qualitative Pressure-Enthalpy Path
The diagram shows process order and pressure level, not exact thermodynamic coordinates.
specific enthalpy h
pressure p
high pressure side
low pressure side
1
2
3
4
compression
condensation
expansion
evaporation
How to read it
1 -> 2 Compression
Work raises vapor pressure and temperature.
2 -> 3 Condensation
High-pressure vapor releases heat indoors.
3 -> 4 Expansion
Liquid pressure drops before the evaporator.
4 -> 1 Evaporation
Cold refrigerant absorbs heat and becomes vapor.
Qualitative diagram: process order and high/low pressure regions only.
No numeric accuracy is implied.
07 / 09
Notes: This is a qualitative p-h diagram, so do not read exact numbers from it. The useful information is process order and relative pressure level. Compression raises the refrigerant to the high-pressure side. Condensation releases heat at high pressure. Expansion drops pressure. Evaporation absorbs heat at low pressure. This diagram connects component names to thermodynamic processes.

## Slide 8
Why Very Cold Weather Reduces Capacity
The system still moves heat, but the source is colder and the compressor lift is larger.
1. Less heat available outdoors
Mild day
larger heat absorption
higher source temp
Very cold
less heat to absorb
lower source temp
2. Compressor lift increases
outdoor source
indoor sink
larger temperature lift
more compressor work required
indoor heat demand
Result: lower delivered capacity and often lower COP.
Cold weather limitation is physical: less source heat plus a larger pressure and temperature lift.
No unsupported numeric claim is made; the explanation remains qualitative.
08 / 09
Notes: Explain the two mechanisms separately. First, very cold outdoor air offers less available heat for the evaporator to absorb. Second, the compressor has to lift the refrigerant from a colder source condition to the indoor heating condition, which increases work demand. Together, these effects reduce delivered capacity and often lower COP in very cold weather.

## Slide 9
Troubleshoot by Following the Heat Path
For facilities teams, the cycle diagram becomes an operating checklist.
Airflow
filters, fan, blocked
supply or return path
Coils
ice, dirt, blocked
heat exchange surface
Defrost
outdoor coil needs
clear heat absorption
Mode and valve
heating/cooling role
switch is correct
Lift
outdoor temp and
indoor setpoint gap
START WITH WHAT MOVES HEAT, THEN CHECK WHAT RAISES PRESSURE
A compressor problem is only one possible cause.
First verify the path for heat absorption and release.
Operational implication
Map low output to the cycle before blaming parts.
Technical recap
Heat is moved; work input raises pressure.
Troubleshooting slide is source-consistent and intentionally practical for facilities operators.
09 / 09
Notes: Close with a practical operating frame. When output is low, do not jump directly to blaming the compressor. Follow the heat path first: airflow, coil condition, defrost behavior, mode and reversing-valve behavior, then temperature lift. This turns the system diagram into a facilities troubleshooting checklist.