## Slide 1
Vapor-Compression Heat Pumps
A Systems Explainer for Facilities & Junior Engineering Teams
Evaporator
Compressor
Condenser
Heat is moved — not created.

## Slide 2
What a Heat Pump Does
Moving heat from cold to warm using work input
Vapor-Compression Heat Pump Systems
2
Cold Outdoor
Reservoir
(low-grade heat source)
Heat Pump
(refrigerant cycle)
Warm Indoor
Space
(heat delivered here)
Q_cold (heat absorbed)
W_in (work / electricity)
Q_hot (heat delivered)
Key principle
• A heat pump does NOT create heat from nothing.
• It uses electrical work (W_in) to move heat from a colder place to a warmer place.
• Energy balance: Q_hot = Q_cold + W_in → the heat delivered exceeds the work input.

## Slide 3
Five Core Components
System architecture — evaporator, compressor, condenser, expansion valve, reversing valve
Vapor-Compression Heat Pump Systems
3
1. Evaporator
Low-pressure refrigerant
absorbs heat & evaporates
2. Compressor
Vapor pressure & temperature
rise — work is added
3. Condenser
Hot high-pressure vapor
releases heat & condenses
4. Expansion Valve
Liquid pressure drops &
temperature falls
5. Reversing
Valve
switches heating ↔ cooling
low-P vapor →
hot high-P vapor ↓
← high-P liquid
cold low-P mix ↑
W_in (electricity)
heat from outdoor air
heat to room
Legend: → refrigerant flow (blue) → heat flow (orange) → work input (purple)

## Slide 4
Heating-Mode Refrigerant State Sequence
Step-by-step state changes around the cycle
Vapor-Compression Heat Pump Systems
4
Step 1 — Outdoor Evaporator
Cold low-pressure mixture
→ saturated vapor
⚡ Absorbs heat from outdoor air
Step 2 — Compressor
Low-pressure vapor
→ hot high-pressure vapor
⚡ Work input from electric motor
Step 3 — Indoor Condenser
Hot high-pressure vapor
→ high-pressure liquid
⚡ Releases heat indoors
Step 4 — Expansion Valve
High-pressure liquid
→ cold low-pressure mixture
⚡ Pressure drop (no useful work out)
↻ Cycle repeats

## Slide 5
Heating vs Cooling Mode
The reversing valve swaps which coil is indoor vs outdoor
Vapor-Compression Heat Pump Systems
5
HEATING MODE
Indoor Coil = Condenser
Releases heat into the room
Outdoor Coil = Evaporator
Absorbs heat from outside air
Comp.
Exp.
heat to room
heat from air
COOLING MODE
Indoor Coil = Evaporator
Absorbs heat from the room
Outdoor Coil = Condenser
Releases heat to outside air
Comp.
Exp.
heat from room
heat to outside
The reversing valve flips refrigerant direction — same hardware, opposite role for each coil.

## Slide 6
COP Formulas & Why COP Can Exceed 1
Coefficient of Performance — the key efficiency metric
Vapor-Compression Heat Pump Systems
6
Heating COP
COP_heating = Q_hot / W_in
Heat delivered ÷ work input
Cooling COP
COP_cooling = Q_cold / W_in
Heat removed ÷ work input
Energy Balance — Why COP > 1
Q_cold (heat from outdoors)
W_in (electricity)
+
= (combined)
Q_hot = Q_cold + W_in
Heat delivered > work input
COP > 1 is possible because the system MOVES heat — it does not convert electricity 1:1 into heat.

## Slide 7
Pressure–Enthalpy Diagram (Qualitative)
The four processes: compression, condensation, expansion, evaporation
Vapor-Compression Heat Pump Systems
7
Pressure P
Enthalpy h →
saturation dome
liquid
vapor
two-phase
1
2
3
4
1→2 Compression (work in, T rises)
2→3 Condensation (heat released)
3→4 Expansion (P drops)
4→1 Evaporation (heat absorbed)
high P
low P

## Slide 8
Cold-Weather Capacity Limitation
As outdoor temperature falls, available heat and capacity both drop
Vapor-Compression Heat Pump Systems
8
Why capacity drops in cold weather
1. Less heat available
Outdoor air holds less thermal energy at low temperatures — less heat to absorb.
2. Compressor lift increases
The pressure (and temperature) difference between cold evaporator and warm condenser grows.
3. Result: capacity & COP fall
The system delivers less heat per unit of electricity. Below the balance point, backup heat is needed.
Capacity vs Outdoor Temperature (qualitative)
Capacity
Outdoor temp →
Heat pump capacity
Building heat loss
balance point
backup heat needed

## Slide 9
Practical Troubleshooting & Operating Implications
What facilities teams should watch and maintain
Vapor-Compression Heat Pump Systems
9
Compressor = Largest Electrical Load
Monitor compressor power draw. A sudden spike can signal refrigerant
overcharge, restricted suction, or bearing wear. Track kW vs. baseline.
Refrigerant Charge Affects Everything
Low charge → low capacity, low COP, risk of evaporator freezing.
Check superheat / subcooling; look for frost on suction lines.
Coil Cleanliness = Heat Transfer
Dirty coils add thermal resistance: evaporator can't absorb heat,
condenser can't reject it. Clean filters and fins seasonally.
Defrost & Cold-Weather Readiness
In heating mode, outdoor coil can frost up. Confirm defrost cycle
works. Below balance point, verify backup / auxiliary heat stages.
Takeaway: a heat pump moves heat efficiently — but only when charge, airflow, and defrost are maintained. Capacity falls in cold weather; plan for backup heat.